## Slide 1: Amateur Radio Emergency Communications Basic Training
ALACHUA County ARES/RACES EMCOMM Training Northern Florida Section ARRL Original Training Presentation developed By AD7FO Spokane County AEC
ARRL EC-001
March 29, 2014

## Slide 2: What is a Communication Emergency
Occurs when a critical communication failure exists that puts the public at risk.
A variety of circumstances can overload or damage critical day to day communication systems…
    Storms that knock down communications infrastructure or lines
    Fires in telephone equipment buildings
    Vehicle penetration into 911 communications center
    Buried fiber optic cable cut by backhoe
    Disruption in power
    Terrorist attack
    Disaster like earthquakes, tsunami's, hurricanes, ice storms, forest fires, volcanic eruptions, etc
LU 1

## Slide 3: ARES/RACES EMCOMM Volunteers
Volunteers come from a wide variety of backgrounds and have a wide range of skills.
Share a desire to help others without personal gain of any kind
Train and practice to improve their communication skills
Can work together as a team and take direction from others
Can think and act quickly under the stress and pressure of an emergency
LU 1

## Slide 4: Where does Amateur Radio Fit In?
A Skilled and equipped communications resource for our Served Agencies*
We do Public service events to practice our skills (March of Dimes, Five Points Marathon, Veteran’s Day Ceremony, Operation Santa Delivery)
We do practice drills with our Served Agencies to improve our skill in a more realistic scenario and to demonstrate our skills
We are not a single communication channel, system or network, we are dynamic and can adjust to the needs of the situation
* Served Agencies are those we have commitments both local and national through ARRL agreements to provide communications when called upon like NOAA (SKYWARN), Red Cross, Emergency Management, Hospitals, etc.
LU 1

## Slide 5: Where does Amateur Radio Fit In?
We are “communications commandos”
We are licensed and have allocated frequencies for local, national and international communication
We can dynamically enlarge and expand our communications network as the situation changes.
We practice many of the needed skills for emergency communication in our daily amateur radio activates
    Directed nets
    HF communications, Changing bands as necessary to maintain communication
    Field Day
    Mobile operation
LU 1

## Slide 6: What Amateur Radio ECOMM is not
We are not first responders, will not be the first on scene
We have no authority and can not make decisions for others
It is your decision if you can participate or not, especially if these decisions affect your own health and welfare
You are not in charge
You are there to temporally fulfill the needs of a Served Agency who's communication system is unable to do it’s job
It is not your job to backfill another job when the agency is short of personnel. Your job is communications. You can however help in other areas if you are qualified and do not compromise your primary job of communications
LU 1

## Slide 7: Day to Day versus Emergency Comm.
In day to day communications there is no pressure to get a message through and no one’s life is dependent on your getting a message through
Emergency communication can involve non-Amateurs and Amateur operators working together
Emergency operations occur in real time and can not be put off to a more convenient time
Emergency communications must be staffed and set up quickly with little or no warning
Following net protocol and giving short, concise messages is imperative
LU 1

## Slide 8
Unlike home operations, emergency stations must be portable and easy to set up quickly
Emergency operation may carry over several hours to several days
Emergency communicators may need to interact with several organizations simultaneously
Emergency communication fills in where commercial systems fail from not having enough reserve capacity. Amateur radio operator skill, equipment, and knowledge can create additional communications capacity in a very short time
Day to Day versus Emergency Comm.
LU 1

## Slide 9: Communicating is job #1
While we are skilled operators, with impressive equipment, and systems in place, our job is to communicate for our Served Agency by any appropriate communication method available to us
If asked to pass a complex message or detailed lists and a fax machine is available then it might be a better choice than radio voice communication.
Always use the best method available and appropriate for the traffic that needs to be communicated
If the target recipient only has an FRS radio or CB radio it would be appropriate to use them. Our message handling skills will work on any communication link, including using a telephone
LU 1

## Slide 10: A Communications Emergency Anatomy
In early phases of many disasters there is no immediate need for communications services. This phase might occur during a severe storm watch.
You can use this time to monitor the situation to prepare to deploy if and when a request for assistance comes.
Once a potential need for more communications resources is identified, a Served Agency will put out a call for volunteer communicators.
You could be asked to operate from an emergency operations center or field location.
Do not count on electrical power being available at the location you are sent to.
LU 1

## Slide 11
In some ARES/RACES organizations there is a designated Rapid Response Team (RRT) that can deploy with a minimal capability in a very short time. The RRT would be backed up by a more robust response in an hour or two.
In a larger response a resource or logistics team may be needed to coordinate incoming volunteers and resources to direct those volunteers and resources to where they are needed most.
In a large event there may be multiple nets in operation on different frequencies.
A Communications Emergency Anatomy
LU 1

## Slide 12
As an event progresses traffic may increase, be sure you prepare for this during the initial phase when traffic is lighter.
For a long term event, operator rotation, food & water, and sleeping accommodations will need to be considered.
Communications Emergency Anatomy
LU 1

## Slide 13: LU1 Review
A communications emergency exists when critical communications systems fail or are not available and the public is put at risk.
At the end of a communications event or exercise it is important to review the effectiveness of the response and look for ways to improve the next time.
It is not appropriate for an emergency communicator to make demands on the agency being served.
The function of a Rapid Response Team (RRT) is to deploy a quick response in a short time.
Do not use person to person voice (grapevine) to transmit you messages.
LU 1

## Slide 14: Amateurs as professionals The served agency relationship
Your attitude is everything! It is more important than your radio skills and equipment. Historically speaking attitudes of some Amateur Radio volunteers has been our weakest point. As one Served Agency once put it “working with ham radio operators is like herding cats”
Although our name says “amateurs” it’s real reference is to the fact that we are not paid for our efforts. We are professional and have the skills and equipment to do an excellent job when called upon.
LU 2

## Slide 15: Who Works for Whom
When serving an agency keep in mind that we are and are viewed as un-paid employees of that organization. If we keep this in mind our relationship with the agency will be on track.
It does not matter if you are an ARES/RACES member or one of the agencies regular volunteer force, they will treat us the same.
It is a misconception that volunteers do not need to take orders. You are expected to comply with instructions from a Served Agency as long as you are able to carry them out safely and do not constitute something that is against FCC regulations (such as going onto the police frequencies).
LU 2

## Slide 16: Professional Emergency Responder View
Unless a positive long term relationship exists between the professionals and volunteers, Professionals are likely to view the volunteers as less than useful. They do not want to do OJT (On the Job Training) during an emergency event and need to know they can depend on the folks they are working with.
Volunteers may be viewed as “part-timers” whose skill level and dedication can not be depended upon when needed.
Working successfully with our Served Agencies during drills and exercises can make a big difference in the way ARES/RACES operators are viewed.
LU 2

## Slide 17: Performing Non-Communication Roles
It has been said that it is a hard and fast rule that communication should be our only role. The answer is yes and no.
In today’s fast paced emergency responses there is not enough time for a rigid set of rules. Communication must move at the same speed. Today’s reality is that any job that involves communication may be what we are asked to do. For this reason we need to have an understanding of what our Served Agencies expect of us.
LU 2

## Slide 18: Typical Radio Roles We Might Perform
Radio operator using Amateur or Served Agency radio systems.
Dispatcher organizing the flow of personnel, vehicles or supplies.
Field observer watching and reporting weather or other conditions.
Damage Assessment, recording & reporting conditions.
Searcher, providing communications for a search and rescue team.
LU 2

## Slide 19: Specific Agency Relationships
At a national level ARRL has agreements in place with many agencies:
    Memorandums of Understanding (MOU’s)
    Statements of understanding, (SOU)
    Statement of affiliation (SOA)
Some of the agencies where agreements exist are:
    Red Cross
    Salvation Army
    Department of Homeland Security
    Federal Emergency Management Agency (FEMA)
    NOAA/National Weather Service - SKYWARN
    Local Department of Emergency Management (DEM)
LU 2

## Slide 20: Talking to the Press
Do Not Talk to the Press
The press is looking for any information they can find and you will most likely know something they would like to know.
It is not your role to be disseminating information to the public. There will be a Public Information Officer assigned to the event or as part of the responding agency you are serving. Refer all questions from the press and others to the event or agency to the PIO.
No matter how persistent the questioner is you are not authorized to disseminate information. If they do not leave when asked, talk with your ARES/RACES or Agency management personnel and ask them to resolve the problem.
LU 2

## Slide 21: Operating Where You Are Not Known
When you are in an area away from home monitoring a local net and hear an emergency call for local ARES/RACES members, do not just show up.
If you are willing and able to help, check into to the net and advise the net control your capabilities and your availability. They will determine if you can be utilized.
Do not be offended if your offer to help is refused. The local net control is thinking about his/her team dynamics, operator skill level needed (yours is unknown to them), specialized training, whether or not more operators are required, local access credentials (background checks) and insurance issues.
LU 2

## Slide 22: Workman compensation & Legal Issues
In some States Workman's Compensation is extended to volunteer workers working on behalf of a government or non profit organization. This is a complex issue and needs to be explored in advance of a call out.
Volunteers providing services to government agencies are provided immunity from liability by federal law through the Volunteer protection act of 1997, 42 U.S.C. section 14501. There are exceptions, check details of the act before assuming your activity is covered.
LU 2

## Slide 23: LU2 Review
Your main job as an emergency communicator is as a radio operator using amateur or Served Agency radio systems.
In the role of a modern emergency communicator you may be asked to serve any function that includes communication.
If you are asked by the Served Agency to do a task that falls outside the FCC rules, discuss the situation with them and develop an alternative solution.
LU 2

## Slide 24: LU2 Review
5. If you are operating as an emergency EMCOMM group and receive an inquiry from the press refer them to the Served Agencies PIO (Public Information Officer).
6. Your attitude will have the most effect on your relationship with a Served Agency
LU 2

## Slide 25: Network Theory The Design of Emergency Comm. Systems
The study of information transfer between multiple points is known as “Network Theory”
Network theory can be thought of as the process of matching a particular message to the best communication pathway. The best pathway efficiently transfers the information utilizing the minimum of the available communication resources while accurately and dependably transferring the information.
By participating in Served Agency emergency planning hams can incorporate fundamental concepts of network theory into their plans so that appropriate modes and resources are available for a real emergency
LU 3

## Slide 26: Single vs. Multiple Destinations
In most cases our communication is from one person/site to another. This is point to point communication that may be monitored by other sites or individuals who need to know what is going on, or who may be able to provide requested resources.
Messages for multiple destinations are called broadcast messages. This might be a weather advisory that is of interest to everyone or an open request for resources from anyone on the net.
LU 3

## Slide 27: Message Precision vs. Accuracy
Precision is not the same as accuracy. Accuracy is important in all our message handling.
  “The hiker has been found in the meadow and in good health” some mistakes in this message at the character level (spelling) will still allow the information to be accurately received and understood.
  A list of names, request for medical supplies, etc require precision at the character level when being sent or received, especially when voice communication is used.
It is important to understand the level of precision needed. Packet is a good choice for high precision messages but may be to cumbersome for simple communication where voice is quicker and easier.
LU 3

## Slide 28: Complexity -Timeliness - Priority
Detailed instructions may be simple to send via voice but if the instructions are too long, the person on the other end may not get it correct. Precision may not dictate written communication, but complexity might.
Timeliness of a message needs to be considered. As you plan your message transmission order, consider if a delay can be tolerated or not.
Priority traffic: If you receive a message that you are told is a priority message, stop what you are doing and send it immediately by the fastest appropriate method.
LU 3

## Slide 29: Communication Methods
Telephone- (land line and cellular)
  One to one
  Requires infrastructure
  May be overloaded
  Not good for high precision messages
  May not have coverage (cell phones)
Fax
  Utilizes phone network
  Good for high precision messages
Two way Voice Radio
  One to one or broadcast messaging
  Not good for high precision messages
LU 3

## Slide 30: Communication Methods
Trunked Radio systems
  Already at high utilization, and sky rocket during an emergency
  Radios (users) have assigned priorities, getting a higher priority requires reprogramming the radio
Packet Radio
  Good for high precision messages
  Can provide permanent record of message (printed/stored)
  Good for broadcast messaging (multiple addresses)
  Easily forwarded to another station (with or without notes)
  May not be reliable for marginal transmission paths
  Not good for graphics transmission
LU 3

## Slide 31: Communication Methods
Store and forward systems
  Bulletin boards
  Mailboxes
  Good when sender and receiver are not simultaneously available
Other
  ATV –Amateur TV (fast and slow scan)
  Satellite communication
  Internet
  Human courier
LU 3

## Slide 32: Planning and Preparation
The key to successful emergency communication is effective planning and preparation.
  What kind of information will need to be communicated?
    Long detailed messages
    Simple status checks, information, questions
    Maps or other graphic content
    How frequent will messages need to be sent and received
    Think about where you may be deployed and how you would operate from there. (Special Needs: Food, Water, Medications?)
    Think about the problems you will encounter and plan to handle them in advance
    Go kits for simple communication and more complex communication such as packet and Win Link-2000
    Periodic checks on the gear and supplies in you go bags
LU 3

## Slide 33: LU3 Review
A secure mode should be used to communicate a list of injuries or causalities
Fax would be good for sending high precision, lengthy and complex messages, and graphics like maps.
A packet bulletin board would be good for non time critical messages and reference material when sender and receiver can not be available simultaneously
LU 3

## Slide 34: LU3 Review
4. The pitfall of Telephones, Cellular Phones and Trunked Radio systems is that they all require a complex central switching system that is subject to failure in a disaster situation
5. Sending a shelter list via an office FAX would be an example of efficient communication. Remember efficient communication does not need to involve a radio.
LU 3

## Slide 35
To be effective in an emergency situation;
  Your team must know and trust each other and each others capabilities
  Must understand their role as a leader or follower
  Must be able to solve problems that arise
ARES® provides structure, training and practice to accomplish the above. ARES® has been part of the ARRL since 1935
LU 4
Emergency Communication Organization & Systems

## Slide 36
Unless a positive long term relationship exists between the professionals and volunteers, Professionals are likely to view the volunteers as less than useful. They do not want to do OJT (On the Job Training) during an emergency event and need to know they can depend on the folks they are working with.
LU 4
Emergency Communication Preparation/Training

## Slide 37
The key to successful emergency communication is effective planning and preparation.
Organization is critical to any emergency response. Without an organization that plans and prepares in advance, an Amateur Radio emcomm response is likely to be disorganized and ineffective
LU 4
Emergency Communication Planning & Organization

## Slide 38
Northern Florida ARES Organization
ARRL Northern Florida Section
Paul Eakin, KJ4G
WB4OMM
Steve Szabo
W4UFL
Jeff Capehart
Santa Fe District
From
Surrounding
Districts
W4UFL
Jeff Capehart
Alachua County
From
Surrounding
Counties
KG4VWI
Susan Halbert
LU 4
DEC
EC
SEC
DEC
EC
SM
WA4JD
Allan West
AEC
AEC
AEC
AEC
AEC
AEC

## Slide 39
Northern Florida ARES Santa Fe District
LU 4

## Slide 40
Created by the Federal Government after World War II
Provides rules to address the need for Amateur Radio operators as an integral part of state, county or local Civil Defense agencies (known as Emergency Management) during a time of national emergencies or war.
RACES has authorization to operate even if the President or FCC suspend normal Amateur Radio operation.
At one point in time some Civil Defense agencies were RACES licensed for Amateur radio with amateur licenses. These are no longer issued, and can no longer be renewed.
LU 4
RACES Radio Amateur Civil Emergency Service

## Slide 41: Other Organizations
Salvation Army Team Emergency Radio Network (SATERN)
  Used for logistical communication between offices and health and welfare messages
  At local level ARES, REACT and other groups help support their radio operations
National Traffic System (NTS)
  Organized and scheduled nets on amateur radio to pass messages, including third party messages.
  Can be used to get messages over long distances
  Trained and experienced at message handling
LU 4

## Slide 42
Military Affiliate Radio Service (MARS)
  Department of Defense Sponsored Auxiliary Communication network
  Three separate managed and operated programs
    US Army
    US Navy/Marines
    US Air Force
  Nets on special assigned/allocated military radio frequencies adjacent to the Amateur bands.
  Special Call signs are issued for MARS use
  Strict rules on message content and structure
  Mars is a backup military, federal, state and local communications network during times of emergency
LU 4
Other Organizations

## Slide 43
Federal Emergency Management Agency (FEMA) &
FEMA National Radio System (FNARS)
  A FEMA high Frequency Radio network designed to provide minimal essential emergency communication capability among federal, state, local commonwealth and territorial governments in time of emergencies.
  FEMA monitors the FNARS frequencies on a daily basis at the state level, typically located in the state emergency Operations Center (EOC).
LU 4
Other Organizations

## Slide 44
National Communication System (NCS)
  A federal agency that consists of 23 government organizations tasked with ensuring the federal government has the necessary communications capabilities under all conditions from normal day to day to national emergencies. The manager of NCA is also the Director of Defense Information Systems Agency (DISA), Usually an Air Force General.
LU 4
Other Organizations

## Slide 45
A variety of government and private emergency communications groups assist in time of disaster. While Amateur Radio groups operators may not interact with many of these systems, it may help to know that they exist, since a served agency with which we may work may utilize or interact with one or more.
LU 4
Emergency Communication may be more than ARES/RACES

## Slide 46
A national EMMCOM group whose operators can be from Citizen Band (CB) radio operators, Amateur Radio, GMRS, FRS, and MURS.
Has an organizational structure similar to ARES with local teams who directly work with some of the same Served Agencies that are supported by ARES
REACT’s mission is somewhat broader that ARES. They can provide:
  Crowd control
  Logistics
  Public education
  May not include communication
LU 4
Other Organizations REACT

## Slide 47
The Emergency Alert System (EAS) is a national public warning system that requires broadcasters to provide their communications capability to the President to National emergency.
The system also may be used by state and local authorities to deliver important emergency information such as AMBER alerts and weather information targeted to a specific area.
Other Organizations Emergency Alert System (EAS)
LU 4

## Slide 48: Organization for rapid Response Rapid Response Team (RRT)
An RRT is a small group within a larger EMMCOM organization that can put a few strategically placed stations on the air quickly
  A level 1 team can deploy within ½ hour of the start of an emergency with short term Jump kits for 12 to 24 hours
  A level 2 team will deploy within hours with more communications and a 72 hour longer term deployment kit that might include:
    Tents, sleeping gear, change of clothes, portable repeaters, extended food and water, personal medications as needed, spare radios, Generator, etc.
  These teams may go by other names such as Quick Response team (QRT), or Rapid Emergency Deployment team (RED team)
LU 4

## Slide 49: Organization ARES Mutual Assistance Team (ARESMAT)
An agreement with other ARES groups to provide assistance and resources in the event of:
  A communications emergency lasting longer than a day or two
  An emergency that requires more resources than are available locally.
Teams consist of hams who are willing to travel to another location
  As an ARESMAT member you are under the direction of the local group that made the request. They are in essence a Served Agency that you are working for.
LU 4

## Slide 50: LU4 Review
The ARES organizational structure is best defined by the ARRL Field Organization as ARRL – Section – District – County
Within a Section, the ARES Chain of command is:
  Section Manager (SM) Section Emergency Coordinator (SEC) District Emergency Coordinator (DEC)
  Assistant District Emergency Coord. (ADEC) Emergency Coordinator (EC) Assistant Emergency Coordinators (AEC)
ARRL Director
Greg Sarratt
W4OZK
KJ4G
Paul Eakin
SECTION MGR
WB4OMM
Steve Szabo
SEC
W4UFL
Jeff Capehart
DEC
W4UFL
Jeff Capehart
ALACHUA
KJ4YPY
Mike Simpson
GILCHRIST
VACANT
LEVY
VACANT
DIXIE
LU 4
Assistant DEC

## Slide 51: LU4 Review
            A level 2 RRT (Rapid Response Team) responds within a few hours and is prepared with 72 hour jump kits for a longer duration of service.
            An ARES Mutual Assistance Team (ARESMAT) is an ARES team willing and able to travel to another area.
            A REACT teams resources may include CB, Amateur Radio, GMRS, FRS, and MURS radio equipment
LU 4

## Slide 52: Served Agency Communication Systems
Most Served Agencies may have their own equipment ranging from modest to complex.
You should work in advance with the served agency to determine if you will bring and operate your equipment or use theirs.
Served Agency equipment may be quite different than Ham Radio Equipment. You will need to understand how to operate it.
Operating protocol and terminology may be different. Practice drills will help prepare you to use served agency radio equipment.
All communication needs to be succinct and professional – no casual conversations.
LU 5a

## Slide 53: Served Agency Communication Systems
Potential Served Agency Systems
  Medical Radio Systems
    HEAR System
    Newer Hospital Emergency Radios have 10 UHF duplex frequencies and 7 VHF simplex frequencies
    Amateur Radio installed at SHANDS
  American Red Cross – National Freq 47.42 MHz
    ECRV Vehicle as well as ERV vehicles
    Chapter Radios
  Police Public Safety groups moving to a new digital communications system, APCO-25
  Emergency Management (EM)
    Communications Trailer
LU 5a

## Slide 54: Communication Systems
  There are three types of shared or multiple user radio systems you may encounter:
    Community (or city wide) repeaters where multiple using agencies share the same repeater frequencies. The users are differentiated by CTCSS tones from the repeater. You must press the monitor button on your radio to see if the frequency is in use by another agency before transmitting.
    Shared simplex frequencies which share the same concept of differentiating users by CTCSS tones except on simplex. Again press the monitor button to insure the frequency is not in use before transmitting.
LU 5a

## Slide 55: Communication Systems
  Trunked Radio Systems
    In a trunk radio system, all users share a pool of frequencies from five up to a maximum of twenty-eight. Users are assigned a "group id" and field radios are programmed to only pick-up transmissions for that group. A computer, called the "site controller", automatically assigns a frequency for users belonging to the same group to communicate with each other. This is done over a data channel called the "control channel", which carries data that tells field radios what frequency they are on. Trunk radio systems may have one or more control channels.
LU 5a

## Slide 56: Communication Systems
Trunked Radio Systems
  Since communications on a Trunked System never stay on one frequency, monitoring these communications with a conventional scanner is virtually impossible, especially in large metro areas where a Trunked System can have dozens and dozens of users.
  Because Trunked Systems require complex repeaters and radios in addition to designated/reserved frequencies they are not currently used for amateur radio communication
  Trunked systems can prioritize users when there is a lot of traffic
LU 5a

## Slide 57: Served Agency Communication
Additional Communications Equipment you may be asked to operate
  Fax Machines
  Copiers
  Computer terminals – To send or forward messages via e-mail
LU 5a

## Slide 58: Disaster Preparedness
Neighborhood Watch Program
Homeowners Association
Community Emergency Response Team (CERT)
Local Disaster Response Training
Preparedness classes
DHS/FEMA ICS (IS-100) & NIMS (IS-700)
LU 5b

## Slide 59: Community Emergency Response Teams (CERT)
Trains in light search and rescue
IS-317 Introduction to CERT
Classroom training course taught by Emergency Management
LU 5b

## Slide 60: LU5 Review
When emcomm members are called upon to operate on public safety radio they may not engage in casual conversations.
Motorola’s trade marked name for CTCSS is PL or Private line
The newer medical emergency medical radio service uses 10 UHF Duplex frequencies and 7 VHF simplex channels.
Amateur Radio does not currently use (or allow) the Trunked Radio System format.
LU 5a

## Slide 61: LU5 Review
5. When EMMCOMM teams work with Served Agencies the Served Agency must provide training if Amateur Radio operators are to be used effectively.
  6. Amateurs might contact Neighborhood Watch, Homeowners Association, and CERT Teams for community preparedness efforts.
  7. CERT is a volunteer program of trained people operating in teams under ICS protocols.
LU 5a &5b

## Slide 62: Basic Communication Skills
The job of an Emergency Communicator is to get the message through to an intended recipient quickly and accurately. Your ability to do this may be limited by:
    Operator Skills
    Communication method
    Noise –Electrical in the transmission path and acoustical at the receive and transmit site when voice is used.
Important skills for a communicator are:
    Listen - Tune out distractions (use a headset if possible) and when unsure of what you heard ask that it to be repeated.
    Be sure the message you copy is correct, ask for a
    read-back to be sure.
LU 6

## Slide 63: Use Good Microphone Technique
  Speak across the microphone not into it (unless you use a desk mike)
  Use your normal clear, calm voice. Do not raise you voice or shout
  Determine the voice level and microphone gain that works best for you
  Wait a second or two after keying the Microphone before speaking to allow the repeater to come up
  VOX is not recommended for emergency communication
  Pause between transmissions to allow for emergency traffic
  Remember if using a repeater most have a 3 minute time out, but try to limit your transmissions to one minute then break to check for emergency traffic
LU 6

## Slide 64: Use Plain Language
Do not use slang or jargon (technical slang)
Do not use Q signals in voice transmissions
Use simple language; “big words” may not be understood by all
Avoid words and phrases that carry strong emotion
Use Proper Phonetics:
A- Alpha I- India Q- Quebec Y- Yankee
B- Bravo J- Juliet R- Romeo Z- Zulu
C- Charlie K- Kilo S- Sierra
D- Delta L- Lima T- Tango
E- Echo M- Mike U- Uniform
F- Foxtrot N- November V- Victor
G- Golf O- Oscar W- Whiskey
H- Hotel P- Papa X- X-ray
LU 6

## Slide 65: Use Pro-words
Clear- end of contact
Over- used to let a specific station know when to respond
Go ahead- Used to indicate that a station(s) may respond
Out- Leaving the air, will not be listening
Stand by- A temporary interruption of the contact
Roger- Indicated the transmission has been received correctly and in full
LU 6

## Slide 66: Using Tactical Calls
You do not need to know called stations FCC call sign
Makes the function/station location you are calling clear
Avoids confusion during shift changes
Use tactical call signs for public service and emergency events
You still need to identify with your FCC call sign every 10 minutes
Identifying at the end of each transmission will indicate the end of transmission and insure you meet the FCC identification rule
LU 6

## Slide 67: LU6 Review
In emergency communication listening is 50% or greater, not 10%
When transmitting, talk across the microphone rather than directly into it
In emergency communications never use 10 codes on Amateur Radio
On a tactical net it is still necessary to identify with your call sign at a minimum of every 10 minutes and at the end of your last transmission.
Giving your call sign is the most effective way to end an exchange on a tactical net.
LU 6

## Slide 68: Introduction to Emergency Nets Information:
The Purpose of any net is to provide a means for orderly communication within a group of stations
An emergency net is a group of stations who provide communication to one or more Served Agencies or the General public in a communications emergency.
LU 7a

## Slide 69: Introduction to Emergency Nets Information:
A formal or directed net is one with a NCS (Net Control Station) who organizes and controls all communication on the net. To send a message you must ask permission from the NCS. Then NCS will authorize message transfer in an orderly fashion, frequently on another frequency, based on message priority. Directed Nets are the best format when there are a large number of stations and/or a lot of traffic.
LU 7a

## Slide 70
On Open (Informal) Nets, the NCS is optional allowing stations to call each other directly. The NCS, if there is one, steps in only if necessary when there is a large amount of traffic or problems arise. Open Nets are usually used when there is little traffic and only a few operators.
Most of the local ARES / RACES activities will use formal nets.
Introduction to Emergency Nets Information:
LU 7b

## Slide 71: Introduction to Emergency Nets Types of Nets:
Traffic Net – Handles formal written traffic in a specified (ARRL) format. Traffic Nets operated by the National Traffic System (NTS) are excellent examples of how an ARES / RACES formal traffic net should operate.
Tactical Nets are used for real time coordination of activities related to the emergency. A tactical net usually has an NCS but may be directed or open.
Resource or Logistics Nets may be needed to acquire resources (food, water and other supplies), accept volunteer check-ins and hand out assignments. This is usually a directed net.
LU 7a/b

## Slide 72
Information Nets are usually Open Nets used to collect and share information on a developing situation without overly restricting the use of the frequency by others. Net members send updated local information as needed and bulletins from Served Agencies.
A good example of an Information Net is a SKYWARN weather net activated during a severe storm.
Introduction to Emergency Nets Types of Nets:
LU 7

## Slide 73
You need to “check in” to a net:
  When you first join the net
  When you have messages, questions or information to send
To become part of a directed net wait for NCS to ask for “check-ins” and listen to any specific instructions such as “check-ins with emergency traffic only”
At the appropriate time (or when directed) check in with:
  Your call sign only
  Your call sign followed by “with traffic”
  Your call sign followed by “with Priority Traffic”
  Your call sign followed by “with emergency Traffic”
  Then wait for NCS to respond before offering more
  information
Introduction to Emergency Nets Checking into an Emergency Net
LU 7

## Slide 74
If there is a long time and NCS has not asked for check-ins and you have traffic or information you may briefly call NCS when there is a break in activity by stating your call sign
If you have emergency traffic do not wait to be called. Call Net Control as soon as there is a break in the conversation
Introduction to Emergency Nets Checking into an Emergency Net
LU 7

## Slide 75
If you are not part of the organization, do not just check in and offer to assist. Listen for a while to understand the situation, what may be needed and what you might offer the organization.
If you feel there is a need and something you can offer to meet that need, you can check-in briefly and ask NCS if there is a resource net in operation, and go there. If there is no resource net in operation make a brief offer of assistance to NCS.
Introduction to Emergency Nets Checking into an Emergency Net
LU 7

## Slide 76
Do not be too surprised if you receive the “cold Shoulder” when checking into a net where you are not a member. The NCS on that net does not know your technical skills or your ability to work with their team. If you have a specific skill you feel may be useful to their operation be sure to mention it.
If offered a menial task, take it, The NCS will get to know you and you could be freeing up a needed member of their team.
Introduction to Emergency Nets Checking into an Emergency Net
LU 7

## Slide 77
When Checking into a net, tell the NCS you have traffic to pass. They will usually ask you to “list your traffic” with it’s destination and priority.
You will not send your traffic until NCS tells you to do so, more than likely on a different frequency. Normally, NCS will tell the receiving station to contact the sending traffic station for traffic.
If you went to another frequency after passing your traffic, return to the net frequency and tell NCS you have passed your traffic so they can remove it from their list.
If using Tactical calls be sure to also add your call at the end of your transmission.
LU 7
Introduction to Emergency Nets Passing Messages

## Slide 78
If the net is in progress and you have emergency traffic to send, you may have to “break” into the net
  Wait for a pause between transmissions and simply say ”break <your call>” and wait for NCS to respond by saying “<your call> go with your traffic”
  You would reply “<your call> with emergency traffic”
LU 7
Introduction to Emergency Nets “Breaking” into the net

## Slide 79
Always let NCS know you are leaving the net, even if it is for a few minutes. If you do not respond NCS may become concerned and be forced to use valuable resources to check on you.
There are three reasons for leaving a net:
  The location of your station is closing
  You need a break and there is no relief operator
  You have turned the station over to another operator (be sure to tell NCS the new operator’s name and call).
LU 7
Introduction to Emergency Nets Checking out of an emergency net

## Slide 80
If you are asked to shut down or move your station by someone in authority, do so immediately. Do not wait to notify NCS. There is usually a good reason for such a request, such as you could be in danger or there may be explosive vapors that could trigger with RF energy.
As soon as you have moved or given permission to transmit and can do it safely, let NCS know what happened and your current status.
LU 7
Introduction to Emergency Nets Checking out of an Emergency Net

## Slide 81
Network systems are often Layered for greater operating efficiency. These Levels could be:
    By Area (LOCAL, County, National)
    By Function (Command, Traffic, Logistics, etc)
    By communication medium (UHF, VHF, HF, Packet, ATV)
Nets do not have to be voice nets. They can be CW, Packet, PACTOR, AMTOR, and more. Many in the Emcomm community are experimenting with HF,VHF PSK31 and WinLink-2000.
LU 7
Introduction to Emergency Nets Levels of Nets
VHF NET
UHF NET
HF NET
PACKET NET

## Slide 82: Review
A net can be best described as a group of stations who gather on one frequency with a purpose.
Directed nets are used when the volume of traffic is too great to be handled on a first-come, first served basis.
A tactical net would handle non-formal communications for a served agency.
LU 7a

## Slide 83: Review
The major difference between an “open net” and a “directed net” is the presence or absence of full control by a Net Control Station.
A tactical net may be directed or open but usually will have a Net Control Station.
LU 7b

## Slide 84: Review
You should check into an emergency net when you first join the net or when you have messages, questions or relevant information.
The most frequent cause of errors on voice nets is speaking too rapidly.
LU 7

## Slide 85: Net Operating Guidelines Net Control Stations
Every organization needs an executive level manager to ensure everything runs smoothly. For an Emergency Communication Net this is the NCS (Net Control Station).
The NCS is the “ringmaster” or traffic cop”. The NCS decides what happens and when it happens on the net.
NCS can be located anywhere but should be in a location where they can hear everyone else on the net.
LU 7c

## Slide 86: Net Operating Guidelines Net Scripts
Nets are usually opened and closed with a standard to ensure the net will operate in a similar format every time. Typical net script format includes:
  Opening –
    <your call>, name and purpose of net, and type of traffic that will be passed.
    If a repeater is being used the frequency, offset and tone are usually given
    Rules or procedure to break for emergency traffic
  Closing
    Thank Participants
    Time and date of net closing
    Return Repeater or frequency to normal use
LU 7c

## Slide 87: Net Operating Guidelines Acting or Fill-in NCS
Filling in for an NCS to relieve them for a short time can be excellent training.
  Watch what the NCS does and you will be able to do it.
  This is not a military operation, treat members with respect .
  Speak Clearly in a normal tone of voice.
  Make instructions clear and concise.
  Keep notes of what is going on.
  Have stations pass traffic on an alternate frequency.
LU 7c

## Slide 88: Net Operating Guidelines Relay Stations
When NCS cannot hear one of the stations on the net because of their location they may ask one of the other stations on the net to relay information back and forth.
Liaison Stations
When it is necessary to coordinate with another net, NCS will assign a liaison station role.
The liaison station role is to pass messages between the two different nets.
This can be periodic check-in interval for coordination or continuous monitoring of the other net.
The other NCS may also assign a Liaison Station.
NCS
A
NCS
B
LU 7c

## Slide 89: Net Operating Guidelines Net Members
Operators at each site are responsible for messages to and from their location.
Must listen to all traffic on the net and maintain contact with the Served Agency.
Whenever possible there should be two members at each site (one can log while the other operates).
Use Relay Stations to reach members of the net that can not make direct contact with NCS.
LU 7c

## Slide 90: Net Operating Guidelines Other Modes Than Voice
Digital modes can have some advantages for an Emergency Net
  Packet modes like FM Packet, HF Packet and PACTOR can provide automatic connection between two stations.
  Provide some security since most folks with scanners will not be able to read your messages.
  Does not require an NCS.
LU 7c

## Slide 91: Net Operating Guidelines Other Modes Than Voice
Keyboard to keyboard packet, PSK31, AMTOR and GTOR can be used
  May require an NCS station
CW with experienced operators can be very effective.
  Clean and accurate code is better than 30 wpm sloppy code
  Make sure your sending speed is compatible with the receiving stations ability to accurately copy.
LU 7c

## Slide 92: Review
In an EMCOMM operation the NCS is responsible for all aspects of the nets operation.
As acting fill in NCS you should avoid asking stations to pass messages on the main net frequency.
A “liaison station” is a station that passes messages between two nets.
LU 7c

## Slide 93: Review
Packet modes of operation include FM Packet, HF Packet, and PACTOR.
If you are the NCS of a net involved in EMCOMM operations and you notice some other station is intentionally interfering with your net move the net to an alternate frequency (note1)
(note 1) Usually we do not respond to a station that is intentionally interfering with a formal net, if possible ignore them. If they persist, follow number 5 in this review
LU 7c

## Slide 94
FCC prohibits any use of Amateur Radio for the benefit of an employer except under certain limited circumstances:
During Disaster Preparedness Drills
Can be government or non-government sponsored
Can be employees of entities participating
Non-Government Sponsored Drills
Limited to one hour per week
Twice in a calendar year can be up to 72 hours
LU 7d
Introduction to Emergency Nets Emergency Drills
New Ruling:
An ARES member using an employer-provided station to check into a local ARES net as an individual is not necessarily transmitting on behalf of the employer.

## Slide 95: Review
There is no limit on the amount of time a radio amateur can participate in a government sponsored drill on behalf of their employer.
The maximum amount of time a radio amateur can participate in a non-government sponsored drill on behalf of their employer is one hour per week.
LU 7d

## Slide 96: Basic Message Handling-Part I Formal and Informal Messages
Formal Traffic
  Formal traffic is done using the ARRL radiogram form or format.
  Formal traffic messages have all the necessary information for tracking and determining the authorizing or originating person.
  If the message is going through more than just the originator and recipient, formal written traffic is needed to prevent errors.
  Using the standard format in a formal message helps in the accuracy of the received message.
LU 14

## Slide 97: Basic Message Handling-Part I ARRL Radiogram Form
Informal Traffic
  Informal traffic is verbal or written and used when there isn’t time to do a formal traffic message. Informal traffic is more difficult to track and determine originators and authoring persons.
  Some emergency messages are best sent informally in the interest of saving time such as requesting an ambulance for a severely injured person.
  Some messages do not require a formal written message because the message is of low value beyond the moment.
LU 14

## Slide 98: Basic Message Handling Part II ARRL Radiogram Form
Message Preamble
Number: A letter or number assigned by originating message to track messages
Precedence: R -Routine, W- Welfare, P -Priority, Emergency
Handling: Instructions for operators handling and delivering the message (see next slide)
Check: Number of words or word groups in the text of this message (continuous characters with no spaces)
Place of origin: The location (city and state) of party for whom message was created, not necessarily the originating station location
Address: Name, address, city, state, Phone number of intended recipient
Assign a number Number | Priority level Precedence | HX | Originating Station Call Station of origin |  | Number of words Check
Station Call or Tactical place of origination Place of Origin |  |  |  | actual time message originated Time Filed (PDT) | Date originated Date
Address, call sign or tactical destination of message |  |  |  |  | 
Address
LU 14

## Slide 99: Basic Message Handling Part II ARRL Radiogram Form
What goes in the HX Block?
Pro Sign Instruction
HXA (number) Collect land line authorized within (number) miles, unlimited if no number is sent
HXB (number) Cancel delivery if not delivered within (number) hours of filing
HXC Report date and time of delivery to originating station
HXD Report to originating station the identity of the delivering station, plus date and time. Report identity of station which relayed, plus date and time, or if delivered report date and time and method of delivery.
HXE Delivering station get message from addressee, originate message back to sender.
HXF (number) Hold delivery until (number) date
HFG Delivery by mail or landline toll call not required. If toll or expense involved, cancel message and service originating Station
LU 14

## Slide 100
The Message Text
The Check for this message would be 14
the | quick | brown | fox | jumped 5
over | the | lazy | dog | X 10
the | dog | was | asleep | 15
 |  |  |  | 20
 |  |  |  | 25
 |  |  |  | 30
 |  |  |  | 35
Basic Message Handling Part II
LU 14

## Slide 101: Basic Message Handling Part II
Signature and Tracking
Signature
Received From | Station Call | Time (PDT) | Date |  | By Operator (Call )
Sent or Delivered | Station Call | Time (PDT) | Date |  | By Operator (Call) )
Signature
Signature is: Name, Call or Tactical name of originator of the message
Additional information: Used for logging when and from who the message was received and how and to whom the message was re-sent if the message is relayed
LU 14

## Slide 102: Basic Message Handling Part II Sending Voice Messages
Speak at a slow pace that allows receiving station to write it down.
Annunciate words for clarity. Use phonetics if needed.
Use pause in the message sections by saying “break” to allow receiving station to ask for repeats.
For messages where accuracy is critical you can ask receiving station to read back the message.
LU 14

## Slide 103: Basic Message Handling Part II Sending Voice Messages
Do not add unnecessary words or comments to your transmission.
Numbers are spoken individually i.e.: “Three Two One ” not “Three hundred twenty one”
Confirm the receiving station has the message and no further questions before terminating the contact.
End contact with your call sign
W7GBU
LU 14

## Slide 104: Review
The preamble to an ARRL Radiogram message will use the word “Emergency” not letter or abbreviation.
If the preamble to an ARRL Radiogram message contains the letters HXE the delivering station is to get a reply from the addressee.
In the preamble to an ARRL Radiogram message the Time Filed block is usually stated in UTC but during emergencies should always be local time.
EDT
Emergency
LU 14

## Slide 105: Review
The Check block in the preamble to an ARRL Radiogram message contains the count of words in the text of the message.
5. In the text of an ARRL Radiogram message punctuation should only be used when it is essential to the meaning of the message.
LU 14

## Slide 106: Basic Message Handling Part II Message Handling Rules
Do not speculate on anything relating to an emergency. There may be hundreds of people listening in on your communication such as other amateurs, general public and the media (using scanners). Consider more secure methods of transmission like Packet for sensitive information.
Pass messages exactly as written or spoken. Your job as a communicator is accuracy along with speed. When relaying messages do not correct what you believe to be errors. Only the original Author can make changes.
LU 15

## Slide 107: Basic Message Handling Part II Message Handling Rules
Non-standard format messages can be sent using the ARRL message format by placing the entire non-standard message in the text body of the ARRL Message form.
Importance of the Signature
Some items requested in an emergency are of high dollar value or have limited shelf life, and may not be restockable. Without proper authorization, requests may be delayed. Be sure to have a name and title of the sender in the signature block.
LU 15

## Slide 108: Basic Message Handling Part II Message Handling Rules
Apparently misspelled words or confusing words must be sent exactly as received. If you are relaying a message you can ask the sending station for read back to be sure you copied it down correctly.
If you think the message is incorrect or confusing you have the option to send it back to the originator. This is a judgment call and should only be done if apparent error may affect the message meaning.
LU 15

## Slide 109: Basic Message Handling Part II ARRL Numbered Radiograms
ARRL Numbered radiograms are a standardized list of often-used phrases.
To send the standard phrase you would send the letters ARL followed by the number of the phrase you wish to communicate.
A complete list of phrases is contained on the ARRL web site.
When sending the following message “ARL, six , four” (arrived safely at _______) would count as 3 words in the text of the message.
LU 15
LU 15

## Slide 110: Basic Message Handling Part II Modified Message Formats
The ARRL message form can handle most situations, but sometimes Served Agencies may request changes or the use of another form such as ICS-213. Each EMCOMM group should work with their Served Agencies to determine which format best fulfills their needs prior to an emergency call out.
Logging and Record Keeping
An accurate record of formal messages handled and your station operation can be very useful and may be required by law in some cases.
LU 15

## Slide 111: Basic Message Handling Part II Logging and Record Keeping
What do you log?
    All Formal Traffic, important informal traffic
    Time and date received and transmitted/delivered
    Message routing (received from and sent to)
    Copy of the message
    Setup, operation and teardown issues and time.
    Power/communication failures
    Any comments you think may be useful
    As a minimum NCS should be keeping a Log.
Plan for how and who will log before the event, generate forms that you will use in advance.
Your records will help in the debriefing and in critiquing your organizations performance so improvements can be made.
LU 15

## Slide 112: Basic Message Handling Part II Logging and Record Keeping
Your logs should be clear and legible. Others may be reading and using what you log. Printing with neat block letters is recommended.
Logs that may become legal documents should be written with a pen.
Logs kept in notebooks will prevent sheets from becoming lost.
SEND 27 COTS x 24 MEALS x 1 FIRST AID KIT
LU 15

## Slide 113: Basic Message Handling Part II Authoring the message
Usually the Served Agency official will author the message. You can help them to be sure the message will be clear.
Agency officials have the authorization and if you are the author the request may not be approved.
LU 15

## Slide 114: Basic Message Handling Part II Message Security and Privacy
Information transmitted over amateur radio can never be totally secure because FCC rules prohibit us from using codes that obscure the actual meaning of the message.
Anything you transmit may be monitored by the media and can legally be used by them.
This does not mean your communication is public information. You should treat the information you communicate as privileged and private.
LU 15

## Slide 115: Basic Message Handling Part II Message Security and Privacy
Messages that contain personally identifiable information such as names of victims or injured should be sent by FAX, Landline Phone or Served Agency secure links.
While there is no way to ensure our messages are not overheard there are some things you can try
    Use an uncommon frequency
    Use digital modes like PSK31, RTTY, AMTOR
LU 15

## Slide 116: Review
As part of an EMCOMM group handling message traffic in an emergency and given a message with typographical errors, you should forward the message exactly as received.
As part of an EMCOMM group handling message traffic in an emergency you are asked to forward a message in non standard format, you should forward the message exactly as received.
You have been asked to send an ARRL Radiogram dealing with a birthday greeting. The correct way to send this message is “ARL FORTY SIX”
LU 15

## Slide 117: Review
When delivering an ARRL numbered radiogram you should decode the message into plain language.
5. During an emergency, service messages should only be sent for “Emergency” and “Priority” traffic.
LU 15

## Slide 118: The Incident Command System
    The Incident Command System (ICS) is an outgrowth from the early 70’s when multi agency responses to wild fires in Southern California ended so disorganized that it prompted Municipal, State, and Federal agencies to form an organization to review the problems. The problems uncovered were:
    Poor overall organization
    Ineffective communication between agencies
    Lack of accountability
    Lack of single well defined Command Structure and commander
LU 16

## Slide 119: The Incident Command System
The review team originally developed an Incident Command System for wildfires, but the system ultimately developed into an all risk system appropriate all types of fire and non fire emergencies.
The ICS developed by the National Fire Academy (NFA) has been widely recognized as a model and tool for the command, control, and coordination of resources at the scene of any emergency and is used by Fire, Police and other agencies around the country.
LU 16

## Slide 120: The Incident Command System
The ICS has two interrelated parts. They are:
1. Management by objectives
Understanding policies, procedures and statutes affecting response
Establishing incident objectives (desired outcome)
Selecting appropriate strategies
Applying tactics likely to or necessary to accomplish objective
2. Organizational structure.
Flexible organizational structure
One person is in charge of all resources
Tasks are sub divided into four major sections
Operating sections can be scaled up or down as needed
LU 16

## Slide 121: The Incident Command System
In addition to the incident commander there are four major operating sections in an ICS. They are planning, operations, logistics and finance/administration.
LU 16

## Slide 122: The Incident Command System
The Incident Command System (ICS) is a management tool designed to bring multiple responding agencies, including those form different jurisdictions together under a single overall command structure.
ICS is not
A fixed unchangeable structure
A means to take control authority away from agencies or departments that participate in the response.
A way to subvert normal Chain of command
Always managed by the fire department or first agency on scene
Too big and cumbersome for small everyday incidents
Restricted to use by government agencies and departments
LU 16
ICS

## Slide 123: The Incident Command System
The incident commander is usually the most senior on scene officer from the first responding agency. As the incident continues for an extended period or grows the person filling the Incident Commander position may change but the role of the incident commander does not change.
Involvement in any Incident Command System is by “invitation only” – There is no role for “off the street” volunteers. The relationship between an emcomm group to the ICS structure will vary with a specific situation. You may not have any part in the ICS Structure except through your served agency or agencies.
LU 16

## Slide 124: The Incident Command System
Emcomm volunteers are encouraged to learn and understand the Incident Command Structure by completing the on line IS-100 Introduction to ICS training on the FEMA website (let your EC know if you take and successfully complete this class):
http://training.fema.gov/EMIWeb/IS/IS100a.asp
LU 16
Students name

## Slide 125: LU11 Review
The letters ICS stand for Incident Command System
ICS is a management tool for coordinating the resources of several agencies within a single command structure.
The ICS has two inter-related parts. They are management by objectives and organizational structure.
In addition to the incident commander there are four major operating sections in an ICS. They are planning, operations, logistics and finance/administration.
The emcomm group may or may not be a formal part of the ICS structure during an Incident.
LU 16

## Slide 126: Preparing for deployment
When preparing for a deployment or callout, remember the Boy Scout Motto “Be Prepared”. What should you be prepared for? As the Founder of the Boy Scouts Baden Powell said “be prepared for any old thing”. The same preparedness goal applies to emcomm volunteers. Being prepared requires advance planning and having a kit of the things you will need ready to pick up and go. These are called Go Bags or Jump Kits. With out prepared jump kit you will likely leave a critical item or two home or take valuable time looking for items when you are called
LU 17
Radios Antennas Food & Water

## Slide 127: Preparing for deployment
Before planning your Jump Kit you will need to consider:
  How long you might be deployed (12, 24, 72 hrs or more)?
  Will you have reliable power or will you need your own power?
  Weather that might be encountered (en-route and at site)?
  Will food, water and sanitary facilities be available?
  How will you and your equipment get to the site?
  Carrying an 80 AH battery may not be practical if you hike in
  Can some kit items do double duty to save space and weight?
  Will your emcomm post be fixed or mobile?
  Will operating position shelter be needed (tarp, tent, Vehicle)?
  What networks and nets will you operate in?
LU 17

## Slide 128
Your emcomm course book has a list of jump kit ideas on page 74. (there is also a list on the ARES/RACES web site)
LU 17
Preparing for deployment

## Slide 129
It may be efficient to sub-divide your kit into multiple kits so you can take what you need for a particular callout with out carrying everything. Some ideas are:
    Quick deployment kit
    VHF/UHF/HF kit for fixed location
    Accessories and tools kit
    Emergency power kit
    Field Shelter kit
  Pre-planning and physical preparation is the key to an effective and timely emcomm deployment. Check your Jump Kits / Go Bags regularly and rotate perishable items like food and water.
LU 17
Preparing for deployment

## Slide 130
Know the frequencies in your area:
Know the local repeater frequencies and coverage.
Know which repeater will be used and where the nets are likely to be.
Know where the nets may move to in case they experience interference.
Know what simplex frequencies will be used in case of a repeater failure.
In Alachua County the primary frequency will be 146.820 repeater with 146.985 as a backup. Simplex operations may be on 146.550 while 146.520 may be monitored for call-ins. Support net for Red Cross may use 147.420 MHz.
LU 17
Preparing for deployment

## Slide 131
LU 17
Preparing for deployment
Train with our served agencies:
  Learn their expectations/needs
  Learn their operation methods and protocol
  Learn their organization
  Identify possible operating locations
  Determine if radio gear is available and how it operates
  Emergency Management (EOC & Shelters)
  American Red Cross (North Central FL Chapter – Gainesville)
  Hospitals (Shands UF, Shands AGH, N. Fla, VA, Specialty)
  Health Department
  National Weather Service (SKYWARN)

## Slide 132: LU12 Review
Preparing a Jump Kit in advance will ensure you will not leave something at home or lose valuable time looking for critical items when called.
A 12 hour deployment Jump Kit would not contain a camp cot or tent. Your 12 hour Jump Kit would contain an VHF HT or VHF/UHF HT, spare batteries, high energy snacks and bottled water.
Your ID cards and other authorization documentation should be among the most important items to be included in your Jump Kit.
LU 17

## Slide 133: LU12 Review
4. A deck of playing cards is one of the least important items for a Jump Kit.
A Jump Kit should contain:
    A frequency list and net schedules
    Contact information for your group and group leaders (EC, DEC, SEC)
    Key Phone Numbers, e-mail and internet addresses
5. If you are assigned to an emcomm operation location in advance one of the least important things you would need to know is the regular business hours maintained at the assigned location.
LU 17

## Slide 134: Equipment Choices for Emergency Communication
VHF / UHF Transceivers
  The most universal choice for emcomm is the dual band 30-50 watt FM transceiver. This class of radio is generally rugged, reliable and can operate at fairly high duty cycles (an external cooling fan is always a good idea and will prolong the life of the radio).
  A second radio to monitor other nets can be quite useful. This can be an HT or just a scanner programmed for the amateur frequencies likely to be used (many of the newer HT’s have a scanning function built in)
LU 18

## Slide 135: Equipment Choices for Emergency Communication
  When using a second radio be sure to use enough separation between the antennas to prevent de-sensing the monitor receiver when transmitting
Radio Receiver Performance For radios on all bands there are several aspects of their performance that can effect its suitability for emcomm.
    Sensitivity – The ability to receive weak signals- This is primarily a function of the receiver front end noise figure or how much noise the receiver front end adds.
    Selectivity – The ability to reject signals on adjacent frequencies while selecting the desired frequency.
LU 18

## Slide 136: Equipment Choices for Emergency Communication
      Intermodulation Rejection – This is the ability of the receiver front end to prevent undesired signals from causing interference. Intermodulation distortion frequently is caused by interfering signals outside the amateur band. Today's radios have wide frequency range beyond the amateur bands that allow interfering signals into the receiver front end. External bandpass filters solve this problem.
      In the field changing to another frequency will most likely eliminate the problem
LU 18

## Slide 137: Equipment Choices for Emergency Communication
LU 18
HF Transceivers
  Unless you are running QRP HF radios require significant power from emergency generators or large batteries. Having an HF radio with both AC and DC power (external Power supply or battery) is desirable.
  Do not use DC to DC Converters to power HF rigs. They may generate a lot of RF “hash”.
  HF radios with adjustable power output allow the
  use of low TX power to extend battery life and High power when needed to get through.

## Slide 138: Equipment Choices for Emergency Communication
Receiver filters are very important for HF receivers. Choice of filters will depend on the mode of operation (PSK, RTTY, CW and phone).
Digital Signal Processing may be the single most important filtering feature available. Internal and external DSP circuits can allow clear reception of signals that otherwise might not be possible in situations with high RF location or path noise.
LU 18

## Slide 139: Equipment Choices for Emergency Communication
VHF/UHF Antennas –
A good antenna mounted as high as possible is more important than high transmitter power. Gain antennas increase your effective signal strength allowing lower power operation for longer battery life.
A unity gain antenna like a J-Pole with fatter lobes may be better for getting out of a valley
Directional antennas are a better choice for Packet to prevent multi-path interference.
Hand held antennas known as “rubber duckies” have
negative gain (loss). Use at least a ¼ wave flexible
antenna for most operations and a 5/8 wave for more range in open areas.
LU 18

## Slide 140: Equipment Choices for Emergency Communication
HF Antennas – There is no single perfect antenna for HF operation.
  For local operation a simple dipole antenna mounted less than ¼ wavelength above the ground works well and is easy to deploy. This is known as a NVIS antenna. An antenna tunner is required.
  A random length wire antenna with a tuner could also be effective. (needs a good ground connection)
  For long range, wire dipoles mounted high above the ground are effective and if properly constructed will not need an antenna tuner
  A trapped vertical antenna may work and a vehicle mounted antenna (Hamsticks, screw driver,etc.) could also be used.
LU 18

## Slide 141: Equipment Choices for Emergency Communication
Feedline (COAX) –
You will need enough coaxial cable to connect your radios to the antennas.
Open wire feed line is generally not a good choice because of the difficulty of running it into a building and possible undesired human exposure.
For short runs RG58 may be useable but for longer runs use lower loss cable like RG8X, RG8, RG213 or 9913. RG8X is a compromise but because of its ease of transport it can be a good choice.
LU 18

## Slide 142: Equipment Choices for Emergency Communication
Operating Accessories –
Headphones are useful in any location, mandatory in others to avoid disturbing others and where multiple radios are in use.
If you have a VOX (Voice Operated Xmit.) headset/mike, turn off the VOX function and use manual push to talk during emcomm events.
If you need hands free operation consider
a desk microphone with a foot switch
LU 18

## Slide 143: Equipment Choices for Emergency Communication
Batteries –Battery operation is critical for emcomm operations. You can not rely on AC power being available. Choosing the right battery is a function of the anticipated current drain (dependent on transmit power setting) and expected duration of operations. Keep in mind that you may not be able to recharge your batteries in the field.
  The ability to operate your hand held on disposable AA alkaline batteries is a plus. Alkaline AA battery holders are available for most HT’s.
  Have a cable to connect your HT, mobile, or HF rig to other batteries by using Anderson Power Pole connectors
LU 18

## Slide 144: Equipment Choices for Emergency Communication
  For higher power needs, lead acid based batteries are available from a few amp hour capacity to over 100 Amp Hour capacity common types available include:
    Flooded cell automotive type (not recommended) and Marine deep cycle type (recommended).
    Sealed Lead acid (Gel Cells)
    Absorbed Glass Mat (AGM)
  Whenever charging batteries make sure you follow the manufactures or industry standard guidelines. Batteries can be damaged or explode if they are charged with too high a current or too high a float voltage.
LU 18

## Slide 145: Equipment Choices for Emergency Communication
Other Power Sources –
  Solar Panels and controllers
  Gasoline driven generators
  Wind and water driven generators
  Human powered generators
  Vehicle power and charging
  DC to AC inverters to power computers
LU 18

## Slide 146: Equipment Choices for Emergency Communication
Other useful equipment –
  Multi Band Scanners
  A voltmeter to check power sources (with leads)
  FRS/GMRS/MURS hand held's
  Cell Phone* to dial 911 (*does not need to be registered or have service to dial 911)
  Battery operated AM/FM radio
  Weather Alert Radio
  Laptop Computer
  Desk Microphone
  Foot operated transmit switch
LU 18

## Slide 147: Equipment Choices for Emergency Communication
And Most Important:
1. Test your station to be sure it all works and you have all the necessary cables, coax, adapter fittings, charged or fresh batteries. Field day and SET (Simulated Emergency Test) would be an ideal time to verify you have a complete operational station.
2. Be sure you have identified / marked all your items so they can find their way home after the event.
LU 18

## Slide 148: LU13 Review
When Powering HF radios whenever possible use deep cycle batteries rather than automotive batteries.
When setting up a VHF/UHF radio a good antenna is more important than high transmit power
If space and resources permit, a beam antenna has an advantage of maximizing the desired signal path and reducing interference from other stations.
LU 18

## Slide 149: LU13 Review
4. The optimum charging voltage for a 12 volt lead acid battery is two volts more than the rated voltage, or 14 volts
5. The 30 amp Anderson power pole connector can be plugged and unplugged a greater number of times without deterioration than the 10 amp Molex connector found on many VHF/UHF mobile rigs
LU 18

## Slide 150: LU13 Review
6. Statements on ARES deployment clothing are:
  Three years (until Jan. 1, 2013) are being given to “wear out” and replace older clothing
  The recommended standards increase recognition and acceptance of ARES units
  The recommended standards apply only to clothing worn on actual ARES deployments
LU 18

## Slide 151: Emergency Activation
The actual way emcomm volunteers will be notified of an activation will be determined locally and as a function of the emergency. In this lesson we will look at some of the most popular methods.
First every emcomm group should have a formal written plan with its served agency to activate their members when needed.
The plan should be developed in detail and then reduced to a simple check list that both served agency and emcomm managers can keep nearby at all times
LU 19

## Slide 152: Emergency Activation
The plan should detail the circumstances under which emcomm activation might occur and should contain all emcomm member names with phone numbers that are periodically verified and kept up to date.
Possible group alerting systems
  Phone Tree
  Paging (a real pager or an HT with a channel and specific CTCSS tone sent from the repeater)
  E-Mail Activation
  Self Activation (prepare and listen to repeater)
LU 19

## Slide 153: Emergency Activation
I have been notified, now what?
  In most cases go to the emcomm net or meet frequency.
  If heading home to pick up your Go Bag
      Fill your vehicle with fuel
      Pick up supplies you may need for activation
      Notify your spouse and Family about what is happening and set up contact times and method for communication during the activation
  Check in and let NCS know your availability
  Have your Jump Kit / Go Bag ready to go
  Do not go anywhere utill instructed to do so
LU 19

## Slide 154: Review
If a telephone tree is activated and you are unable to reach one of your assigned contacts on the list you should call all of those assigned to the person on the list who could not be reached.
An “emcomm activation liaison” for a served agency is the member of the emcomm group who is alerted first by the agency.
Regarding emcomm alerting systems it is best not to rely exclusively upon any single alerting system.
LU 19

## Slide 155: Review
4. E-mail is best used as a backup alerting
system
5. The NCS (Net Control Station) is so important that several members should be trained to take on the duties until the assigned NCS checks in.
LU 19

## Slide 156: Set Up, Operation & Teardown
If you have a known assignment or are available for assignment check into the net and let NCS know you are available.
Get your equipment loaded up and be ready to go.
When proceeding to your assignment check in with NCS on your progress, especially when travel is hazardous.
LU 20

## Slide 157: Set Up, Operation & Teardown
Check in with the person in charge at your assigned location and tell them who you are, why you are there and what you can provide for them.
If you are asked to brief the staff of a served agency about the privacy of amateur radio you should tell them that there are no methods by which the security of any message can be assured on Amateur Radio
Expect the situation and assignment to be fluid. Each incident is unique and may change quickly.
LU 20

## Slide 158: Set Up, Operation & Teardown
At each station the EC or emcomm manager should appoint one member to take a leadership role as the station manager for all operations at that station.
When you accept the role of an emcomm volunteer you do so knowing you will often need to follow the directions of another person. Cooperation and teamwork are essential.
LU 20

## Slide 159: Set Up, Operation & Teardown
Expect that sometimes you may be a leader and at other times you will be a follower
Plan ahead, if no building or inside space is available for you and your radio gear be prepared to operate out of you vehicle or bring a tent or other shelter.
LU 20

## Slide 160: Set Up, Operation & Teardown
When setting up your gear on a desk, table or other location where someone else's “stuff” is in your way, carefully store it in a safe place, like a cardboard box you can seal, label it so it can be safely stored out of the way until the event is over.
After the event is over place the box of “stuff” back on the desk or table but leave it in the box. Do not try to remember how it was set up or try to place it back that way.
LU 20

## Slide 161: Set Up, Operation & Teardown
Your first order of priority will be getting a station setup and checking in with NCS.
Once your station is on the air and you have checked in with NCS you can check your location to determine what other resources may be available:
  Computer/internet, fax machines, telephone lines
  Determining what frequencies and signal paths are available (repeaters and simplex paths)
  Learn about the Served agency role at this location and their communication needs
  Food Water, Sanitary facility availability
  Setting up additional radios (may need to wait for help)
LU 20

## Slide 162: Set Up, Operation & Teardown
Directions to end operation may come from the served agency or from NCS.
Unless there is imminent danger, when a served agency manager tells you to end operations you should notify NCS before closing your station.
If you had to close the station quickly because of an emergency, contact NCS as soon as it is safe and let them know what is going on.
LU 20

## Slide 163: Set Up, Operation & Teardown
Before leaving clean up the area you occupied and remove any trash, coffee cups and pop cans that accumulated during the event.
After the event collect your messages and notes and save them for an emcomm team debrief session (sometimes your notes and message copies will be turned over to the served agency manager before leaving).
LU 20

## Slide 164: Set Up, Operation & Teardown
After an emergency station operation, your emcomm group (and possibly the served agency) will want to hold a debriefing session.
The purpose of the debriefing sessions is to review what worked well, issues that may have arisen and where improvements are needed for future operations.
Jotting down notes during the event will help your memory for the debrief session that follows the event.
LU 20

## Slide 165: Review
If you have been activated during an emergency and have been told to report to an agency that is different from your usual assignment you should introduce yourself to the person in charge as the emergency communicator assigned to that location
If you are asked to brief the staff of a served agency about the privacy of amateur radio you should tell them that there are no methods by which the security of any message can be assured on Amateur Radio
LU 20

## Slide 166: Review
3. If you have been assigned to a site and the emergency ends and the site manager asks you to close your station; you should you should check in with the emcomm manager or net control before closing down.
4. In preparing to leave a site after an emcomm event you should not unpack all desk items you placed in boxes and put them back in their original locations.
5. The primary purpose for a debriefing after each emcomm event is that affords an opportunity to improve future emcomm activities.
LU 20
Notes: 166

## Slide 167: Operations and Logistics
One of the values Amateur Radio brings to the table is a vast amount of radio spectrum;
Most local and regional emcomm traffic will be on 2 meter and 70 cm FM, or on 40, 60 or 80 meter SSB and CW.
VHF and UHF FM are preferred for most local operation because the equipment is common, antennas are smaller, and communications are clearer.
LU 21

## Slide 168: Operations and Logistics
VHF and UHF communication range is determined by terrain, antenna height and availability of repeaters.
For larger areas or those with out repeaters most local emcomm operation will be on the 40 and 80 meter bands using NVIS (Near Vertical Incident Skywave) antennas.
Your jump kit should have a list of frequencies commonly used for emcomm.
LU 21

## Slide 169: Operations and Logistics
You should become familiar with coverage, and features or each permanent repeater
    Are there dead spots in the repeater coverage?
    How much transmit power required to hit the repeater?
    What features are available (like phone patch, Echo Link etc.)?
    How does the repeater identify?
    Does it have a courtesy tone?
    Does it have a time out, how long, how is it reset?
    Are there inks to other repeater systems?
LU 21

## Slide 170: Operations and Logistics
You should become familiar with coverage, and features or each permanent Packet node, digipeater and other means of digital communication like Packet-Pactor, WinLink, PSK31, RTTY, etc in your area.
    Are there mail boxes?
    Do they have digipeater functions?
    Do they have bulletin boards?
    Which software do they use, how can you communicate through it?
    What other nodes can they connect to?
    How many communications can the support simultaneously?
LU 21

## Slide 171: Operations and Logistics
If all else fails and simplex communications are spotty consider placing a mobile station or portable repeater on a hill top or on the top of a tall building.
Portable Battery operated repeaters are a good resource to have available. They are easily and quickly deployed when and where needed.
Permanent repeaters designated for emcomm use should have backup power available (batteries and/or generator)
LU 21

## Slide 172: Operations and Logistics
In addition to the main net frequency each net should have several alternate frequencies available. A couple in case of interference on the main net frequency and a couple for stations to pass traffic “off net”.
If there is no direct path between NCS and the emcomm station a relay station should be identified to relay incoming and outgoing traffic.
LU 21

## Slide 173: Operations and Logistics
Most served agencies will expect you to keep records of your operations. Your records should include copies of messages received and sent, station log memos and any official correspondence.
In Some agencies your station records are permanent and important legal documents and must be treated as such.
To protect equipment and the messages you handle an prevent distractions it is best to allow only the operators who are on duty to be in the communications room.
LU 21

## Slide 174: Operations and Logistics
Station logs should contain:
  Arrival and departure times
  Times for nets you can you checked into
  Times for nets you can you checked out of
  Message number, sender and addressee
  Special handling instructions
  Critical events (damage, power loss, injuries, earth tremors)
  Other emergencies
LU 21

## Slide 175: Operations and Logistics
An unusual event such as an emcomm emergency response to a disaster can create incredible amounts of stress. When under extreme stress individuals can become:
    Disoriented & Confused
    Unable to make decisions
    Lose their tempers
    Behave in ways they would not at any other time
LU 21

## Slide 176: Operations and Logistics
Extreme stress can lead to nervous breakdowns
  Take a break. You can’t do it all now
  Step back and take a few deep breaths and relax
  Prioritize your assignments and duties
  Delegate some of your responsibilities
  Do not take comments personally \ Look at them as constructive criticism
  Pay attention to your own needs (Food, water, medical needs, sleep)
  If someone is losing control of a situation bring someone else in to assist (or let your manager know they need help)
  Take a minute to think before responding to a stress causing challenge
LU 21

## Slide 177: Operations and Logistics
If operating from battery power you will need to:
    Have enough batteries for the expected duration
    Find a way to recharge them if long operating times are required (may not be practical for slow charge batteries)
    Have standard connectors on the battery and radio
If using a gasoline generator think about it’s placement to prevent Carbon Monoxide from entering inhabited areas and ensure its acoustical noise causes minimum disturbance to others.
LU 21

## Slide 178: Operations and Logistics
LU 21
In the world of modern emcomm you may be asked to handle other assignments for the served agency that may or may not include communications. At one time the answer was a hard and fast “NO”
Today most emcomm groups will let their volunteers be cross trained to perform a variety of served agency skills that also involve communications:
  SKYWARN weather spotting
  Red Cross Damage Assessment
  Red Cross logistics Jobs
  Situations where you could do both jobs

## Slide 179
Operations and Logistics
Some Portable stations used during Katrina ranging from an HT with gel cells to a kilowatt HF station

## Slide 180: Review
Terrain, output power and antenna gain will limit VHF simplex communication range.
Increasing antenna height, increasing transmitter output power and moving the antenna away from obstructions will improve simplex reception (range). Switching to a non-directional antenna will not improve reception.
The FCC rules do not permit unattended operation of simplex repeaters.
LU 21

## Slide 181: Review
Driving a delivery vehicle for a served agency would not be an appropriate assignment for an emcomm volunteer.
5. Prioritizing you actions with the most important and time sensitive first on the list is a good means of dealing with stress during an emcomm event.
LU 21

## Slide 182: Personal Safety, Survival & Health
As a disaster relief volunteer, do not get so involved in helping others that you forget to take care of yourself. You need to keep yourself in good condition so you are able to assist others.
Before leaving home for an assignment be sure you have made all the necessary arrangements for the security, safety and general well being of your family.
Set up a communication plan with your family.
LU 22

## Slide 183: Personal Safety, Survival & Health
In addition to your emcomm checklist you may want to create a home and family checklist.
Some things to consider:
  If you will be without power in an area where it will freeze drain your water pipes.
  Heating fuel tanks should be filled
  Shut off power and gas
  Board up windows
  Move valuables to an upper level
  Ensure your family has reliable transportation with a full fuel tank
  Emergency food and water supply.
  Prescription medications
LU 22

## Slide 184: Personal Safety, Survival & Health
When You leave
  Food (2000 calories a day) Freeze dried camping food, Energy bars, military style Meals Ready To Eat (MRE) and small camp cook stove.
  Water (1 gallon per day recommended, 2-3 liters per day to survive). Questionable water can be purified by adding 2-4 drops (1/8 teaspoon) of unscented liquid Clorox laundry bleach to a gallon of water and leaving it sit for 30 minutes.
  Personal Hygiene items- Tooth paste, tooth brush, deodorant soap or waterless hand cleaner
LU 22

## Slide 185: Personal Safety, Survival & Health
When You leave (continued)
  Prescriptions
  Extra glasses (or safety glasses) in a hard, felt lined case.
  Cash – Do not assume there will be a cash machine or that food an fuel can be paid for with a Credit/Debit card.
  There is a sample personal survival and comfort check list on pages 108 and 109 in your Emcomm I Training manual
LU 22

## Slide 186: Personal Safety, Survival & Health
Safety in unsafe places. Many times you will be sent to areas that can be dangerous and pose safety risks.
  Understand the environment before entering.
  Wear appropriate clothing and if appropriate gloves and boots.
  A hard hat might be appropriate in some situations
  Avoid industrial areas where toxic chemicals nay be stored.
  Always be sure you have more than one exit from your operating location.
  Carry a Police or signaling whistle so you can let rescuers know where you are if you need to be rescued
  Flashlight and if possible a chemical light stick
LU 22

## Slide 187: Review
Water purification tablets will not remove Bacteria and dirt (it will kill bacteria but not remove dirt).
It is best to use two to four drops (or 1/8 teaspoon) of plain, unscented, liquid chlorine bleach to a gallon of water to purify it for drinking.
Keep spare eyeglasses or safety glasses in a hard felt lined storage case in your go bag.
LU 22

## Slide 188: Review
4. Because many disaster assignments are in unsafe places you should always plan more than one escape route from buildings and other hazardous locations.
5. Your personal safety and well-being are a higher priority than the mission.
6. An MRE meal is a package meal that can be stored for a long period of time and requires a minimum of preparation. MRE stands for Meals, Ready to Eat.
LU 22

## Slide 189: ARES PIO: The Right Stuff
Public Information Officer (PIO)
  “Providing the Right information to the Right people at the Right time so they can make the Right decisions” -- FEMA Advanced PIO Course
Agency PIO
  Media Relations
  Part of the ICS Team
  Silence is as bad as errors – rumors start
  ICS standardize ways to be a unified voice
Unified Command (UC) – All agency PIOs report to the Joint Information Center (JIC)
ARES PIO
  Expert on Amateur Radio
  Introduce other ARES members to the Media
  PIO and operators are properly dressed
  Avoid interviews with inappropriate dressed members
LU 23

## Slide 190: Review
A Joint Information Center is established to:
  Formulate a unified voice and message
  Dispel rumors
  Provide a central location for media questions
If a reporter shows up at your ARES deployment, but you’re not the PIO, refer them to the JIC, designated Lead PIO or ARES PIO.
LU 23

## Slide 191: Alternative Communication Methods
Amateur radio may not be the only radio service for the job.
Handing an official a hand held radio to stay in contact with the ARES/RACES team may be better than shadowing the official, epically when the official is involved with sensitive issues.
The amateur radio emcomm team should be equipped to communicate with other communication networks and types.
LU 24

## Slide 192: Alternative Communication Methods
Some of the alternative communication radio services require licenses, others require group licensed and still others require no license at all.
You can easily modify many of today's 2 meter/70cm radios to operate on a nearby public service or business band radio service frequencies. You should think carefully about how you will use the modified radio vs. the risk of accidentally transmitting on a frequency in another service.
LU 24

## Slide 193: Alternative Communication Methods
CB (Citizens Band) radios
  No License required (Can’t ID with your Amateur callsign but you can still use your old CB call if you had one when the FCC issued licenses.)
  AM (Some SSB) - Voice communication only.
  5 watts input to final maximum.
  Operate on 11 meters (26.965-27.405) on 40 assigned channels.
  Used by emergency teams like REACT
  Typical range is 2-8 miles for mobiles, 25 for base to mobile operation,. FCC limits the max allowable range to 75 miles.
  Channel 9 is still monitored for emergency traffic by some emergency responders in more rural areas. Truckers use Channel 19 on the Interstate and other road networks.
LU 24

## Slide 194: Alternative Communication Methods
FRS (Family Radio Service) radios
  No License required
  No Base Stations, only HT’s
  FM voice communication only.
  100-500 mw transmit power .
  Operate in the 462 MHz range
  14 channels with CTCSS tone capability
  Used by emergency teams like REACT
  Typical range is 1-5 miles
  Channel 1 is monitored by REACT for emergency traffic
LU 24

## Slide 195: Alternative Communication Methods
MURS (Multi Use Radio Service)
  No License required (the new Citizens Band)
  Personal and business communication allowed.
  Primarily for mobile and portable use.
  Maximum of 2 watt transmit power .
  Operate on 151-154 MHz, FM Voice only.
  14 channels with CTCSS tone capability.
  Used by emergency teams like REACT.
  Range is similar to a 2 meter hand held on simplex.
LU 24

## Slide 196: Alternative Communication Methods
GMRS (General Mobile Radio Service) radios
  License required – No Call sign
  No Base Stations, only HT’s
  FM - Voice communication only.
  5 watt max transmit power on channels shared with FRS
  50 watts on non FRS Channels
  UHF Frequencies between 462.5625 to 462.7250 MHz
  FM Voice only.
  15 channels with CTCSS tone capability.
  8 channels are paired with a repeater frequency 5 MHz higher.
  No Frequency Coordination or assigned frequency for users.
LU 24

## Slide 197: Alternative Communication Methods
Public Service Radio (Police, fire)
  May allow you to train to use their radios.
  Only use if directed by an officer
  Keep transmissions short.
  Cease transmitting if they tell you to
  Do not modify your radios for these bands.
Cellular and PCS Phones
  In smaller events these may still be viable
  Offer more security than Amateur Radio
  Can Send text messages
LU 24

## Slide 198: Alternative Communication Methods
Marine Radio
  Allocated channels on the 160 MHz Band for Ports and Inland waterways.
  No License requires for US waters operation.
  FM Voice.
  25 watt transmit power
  Chanel 16 monitored by Coast Guard.
  Additional HF Frequencies allocated between 2 and 30 MHz for long range SSB Communication
  IF you hear a vessel and no one is responding you are permitted to answer the distress call and determine the nature of the emergency and relay the message to the coast guard or other authority.
LU 24

## Slide 199: Alternative Communication Methods
Aviation Radio
  108 to 136 MHz (108-118 for navigation, 118-136 MHz reserved for Voice communication). Military aircraft use 225 MHz to 400 MHz
  AM Voice.
  Emergency frequency is 121.5 MHz for commercial aircraft and 243.0 for Military aircraft.
Non-Radio Communication
  Land line telephone if it is still working
  FAX
  Email
  Courier
LU 24

## Slide 200: Review
You can not use your amateur call sign on citizens band even if you were a licensed amateur when 11 meters was an amateur band.
Call at regular intervals on channels 9 and 19 when trying to summon help on a citizens band radio.
FRS Radios are readily available at low cost, operation is simple and requires little training and there is no licensing requirement for FRS. FRS radios have limited range because they have low transmit power and can not be connected to an external antenna.
LU 24

## Slide 201: Review
4. Any individual can license a GMRS system for personal and family use.
5. Data Emissions are not permitted on MURS (Multi-Use Radio Service)
LU 24

## Slide 202: What to Expect in Large Scale Disasters
At the onset of a disaster:
  There is a huge increase of volume in traffic on public service radio channels.
  Prolonged waiting periods to gain access to communications.
  Outages may occur in key areas.
  Messages are not handled in priority order and are sometimes lost.
As additional agencies arrive:
  There is a need for agencies to communicate with each other but may be unable to use each others frequencies.
  Their communication procedures may be different.
  Agencies are reluctant to have others operate their equipment
LU 25

## Slide 203: What to Expect in Large Scale Disasters
.
LU 25
During initial phase:
  Agencies may need to contact others more than 350 miles away.
  Message reply delays lead to deferred decisions on crucial matters.
Different modes of communication are required in addition to voice.
  Volume data in printed form (High speed packet & Fax).
  Morse code and PSK31 for difficult reception conditions.
  Encoded data for privacy.
  Telephone interconnects to and from radio systems.

## Slide 204: What to Expect in Large Scale Disasters
LU 25
During the first 72 Hours of a disaster:
  It takes precious time to overcome obstacles.
  Communication is one of the vital resources that can be difficult.
  The greatest concentration of relief effort is generally found in incorporated cities served by agencies with paid professionals.
  Rural areas suffer because of their remoteness and limited resources.
  Frequently the public is isolated, unable to call out for help or determine what their course of action should be.
  Lack of information leads to further attempts to use the already overloaded phone systems.

## Slide 205: What to Expect in Large Scale Disasters
After the first 72 hours the disaster area usually remains in virtual isolation from the rest of the world.
The American Red Cross is the organization that handles health and welfare on behalf of the victims.
Amateur radio plays an important role of communicating health and welfare information.
LU 25

## Slide 206: Review
The first thing that happens after a disaster occurs is a massive increase in the volume of traffic on public service radio channels.
One of the big issues in an emergency is that agencies all use different frequencies and inter- agency communication is not possible.
The greatest concentration of relief efforts during the first 72 hours of a disaster will be found in urban areas.
LU 25

## Slide 207: Review
4. The American Red Cross is the organization that handles health and welfare on behalf of the victims.
5. In the initial 72 hours following a disaster the disaster area usually remains in virtual isolation.
LU 25

## Slide 208: Hazardous Materials Awareness
LU 26
You may pass through a HazMat (Hazardous Materials) Incident en route to an assignment or be stationed at a HazMat incident.
HazMat materials include liquids, solids and gasses that are corrosive, poisonous , or radioactive, explosive or otherwise hazardous to your health and that of others.

## Slide 209: Hazardous Materials Awareness
LU 26
Proper training is required for your safety around HazMat incidents.
The US Department of Transportation (DOT) is responsible for the safety regulations for the transportation of hazardous materials.
DOT has defined Hazardous materials by a class designation and has established standardized Hazardous material in placards and other markings requirements for vehicles transporting them

## Slide 210: Hazardous Materials Awareness
LU 26
All freight containers, railcars, and trucks transporting Hazardous materials must display the diamond shaped placard identifying the class (or classes) of materials they are carrying.
A commonly seen placard is the one with the number 1203 (Petrol) will be seen on Gasoline tankers delivering fuel to your local service station.
The sign placard with 1993 is for diesel fuel

## Slide 211: Hazardous Materials Awareness
LU 26
The National Fire Protection Association (NFPA) has devised a marking system to alert fire fighters to the characteristics of hazardous materials stored in stationary tanks and facilities. The system is known as the NFPA 704M. In consists of a diamond shaped placard with 4 smaller diamonds.
The numbers in the diamonds represent the hazard to humans on a scale of 1 to 4 (4 being the highest). The colors are
      Red - Fire Hazard
      Blue - Health Hazard
      Yellow - likelihood to explode or react

## Slide 212: Hazardous Materials Awareness
LU 26
You should report what you see if asked, but do not get to close to the HazMat Incident. Information that would be helpful to report would be:
    Location of incident and location
    What kind of incident
      Spill
      Gaseous cloud
      Any visible placards on building, tanks or vehicle

## Slide 213: Review
You should be located as far away as necessary to ensure your safety when in the vicinity of a HazMat incident.
The Department of Transportation is Responsible for warning the public about hazardous materials containers and shipments.
You should be far away so that no vapors or fumes are present before transmitting in the area of a HazMat incident.
LU 26

## Slide 214: Review
4. On the sides of transporting vehicles different classes of hazardous materials are identified by placards, four digit numbers and warning labels or icons.
5. Gasoline tankers filling a neighborhood gas stations underground tanks are identified with a placard bearing the number 1203
LU 26
1203

## Slide 215: Marine Communications
The most common for marine communication is
  VHF FM voice
  Range is 1-15 miles ship to ship
  Range is 20-30 miles ship to shore
  In the 156-162 MHz range
Vessels outside the FM communication range will have MW/HF or satellite radios for communication .
LU 27

## Slide 216: Marine Communications
LU 27
Marine FM radios are marked in channels rather than frequency.
The Marine FM channels are assigned for specific purposes:
    Channel FM 16 – Calling frequency and distress calling frequency.
    Channel FM 9 – Alternate calling frequency.
    Channel FM 83 – Coast Guard Auxiliary.
    Channel FM 22 – Communication with the Coast Guard, but only when specifically instructed to go there.
    Channel FM 23 – Us Coast Guard

## Slide 217: Marine Communications
LU 27
Calling an emergency on a marine radio:
  MAYDAY-MAYDAY - Highest priority distress signal, grave danger, immediate assistance is needed.
  PAN-PAN (pronounced Pawn - Pawn) urgent call concerning safety of vessel or person.
  SECURITE - Official message regarding safety of navigation or weather warnings.
  SILENCE – The Coast Guard may order silence on a specific channel and limit it’s use to activities involved in an incident or emergency.

## Slide 218: Marine Communications
LU 27
The following information should be obtained from the vessel in distress:
  Position of the vessel involved (GPS lat/long if possible)
  Number of persons on board
  Nature of distress
  Name and call sign (if there is one) of the vessel
  Type and length of the vessel
  Description of the vessel including color
  Weather conditions on scene
  If they have an EPIRB or PLB (Personal Locator Beacon) on board and it’s class

## Slide 219: Marine Communications
LU 27
Once you have the information advise all persons to don their life jackets.
Then call the nearest USCG facility or 911. Let them know how to contact you in case you are the only link to the vessel in distress.

## Slide 220: Review
LU 27
It is only permissible to use Marine FM channel 22 when Instructed to do so by the Coast Guard
If you hear a marine distress call and it goes unanswered after listening, you should respond and gather all the information possible then contact the nearest Coast Guard facility
You must identify yourself on all transmissions on a VHF Marine radio

## Slide 221: Review
LU 27
4. Only Seagoing vessels operating outside the range of VHF communication are authorized to transmit on the marine MW/HF SSB frequencies.
5 Marine FM channels 9 and 16 can be used to call another vessel

## Slide 222: Modes, Methods and Applications
You will need to choose the best method of communication for each situation in an emcomm environment.
Communications concepts to consider.
Communications modes fall into several categories:
  Point to point – Telephone and some digital modes
  Multi-point – Voice and CW and some digital radio modes
  High precision – Fax, e-mail and digital modes
  Low precision – Voice, CW and Telephone
  High priority – Voice, telephone
  Low priority – Fax, e-mail, digital modes, CW
LU 28

## Slide 223: Modes, Methods and Applications
Messages fall into similar categories:
  Point to point – Messages intended for one party.
  Point to multi-point – Messages intended for a group.
  Multi-point to point – Messages from group members to one station .
  High Precision – Lists of items, medical or technical terminology, specialized or detailed information.
  High Priority – Fast delivery is critical.
  Low priority – Messages can be delivered in a more relaxed time frame.
LU 28

## Slide 224: Modes, Methods and Applications
LU 28
Each message type should be sent using the most appropriate mode based on the message content and destination.
Remember radio may not be the only means of communication available at a site. For example, if you are at a Red Cross shelter with power:
  Consider using a power supply for the radio to save batteries.
  If fax or telephones or internet are available at both ends use them, but be prepared should they go down on either end to use radio communication.

## Slide 225: Modes, Methods and Applications
225
LU 28
Do not use voice for messages that are long, detailed, or technical in nature if an alternate means or mode is available.
Think about who may be monitoring before sending sensitive or private information. Consider that the press, general public and thieves may be monitoring what you transmit.
  Some modes provide an increased level of security
  No amateur radio transmission is totally secure.

## Slide 226: Modes, Methods and Applications
Digital modes:
    Can be useful in passing large volumes of traffic.
    Can provide error free transmission (many have error correction) of input data, can be saved at either end for re-transmission, printing or archiving.
  What digital modes are available?
    For HF the best digital modes are Packet, AMTOR mode B and PSK31.
    For VHF/UHF The TNC 2 (Terminal Node controller version 2) Packet is the most common
LU 28

## Slide 227: Modes, Methods and Applications
Additional Modes
  APRS for location and short messages
  Amateur TV
    Slow Scan images via HF
    Real time TV on 70 cm and above
LU 28

## Slide 228: REVIEW
Your purpose as an emergency communicator is to provide accurate and rapid transfer of information from one place to another.
Tactical messages are generally low precision and time critical.
Long lists and detailed messages are best handled by FAX or Digital mode transmissions.
LU 28

## Slide 229: REVIEW
4. If absolute privacy is required do not transmit the message by amateur radio.
5. The QPSK mode of PSK31 features error correction.
LU 28

## Slide 230: Other Learning Opportunities
Regularly scheduled nets provide an excellent opportunity to practice net procedure. Nets are also a good opportunity to practice being net control operator.
Local ARES/RACES formal training and both on and off the air.
Public service events and formal training like SET, SKYWARN recognition day and Field Day offer excellent setup and on the air practice.
LU 29

## Slide 231: Other Learning Opportunities
There is additional training and resource material available on the ARRL website that can be downloaded and printed for free:
    ARRL Public Service manual
    ARES Field Resources Manual
    ARRL Net Directory
    Alachua County ARES/RACES web site
Check your training manual for additional resources
LU 29

## Slide 232: Review
Regularly scheduled nets, on air training sessions and public service events are recommended as a means of practicing actual emcomm skills. Discussion groups are not a means of practicing communication skills.
The purpose of the ARRL’s Public Service and Emergency Communications Management for Radio Amateurs course EC-016 is to prepare individuals for management level jobs such as EC, DEC or SEC or other leadership or training roles.
LU 29

## Slide 233: Congratulations!!
You have completed the
ALACHUA County ARES/RACES
ARRL EMCOMM BASIC training class!!!!!